| TIRE AND WHEEL INSPECTION |  | PM#B ADD THE FOLLOWING |  |
| --- | --- | --- | --- |
| CHECK TIRES FOR IRREGULAR WEAR |  | TAKE ENGINE OIL SAMPLE IF REQUIRED |  |
| CHECK TIRES AT WEAR LIMIT |  | CHANGE ENGINE OIL |  |
| CHECK & CORRECT TIRE PRESSURES |  | CHANGE ENGINE OIL FILTERS |  |
| CHECK FOR MISSING VALVE CAPS |  | CHANGE FUEL FILTERS |  |
| CHECK WHEELS FOR CRACKS |  | CHANGE WATER FILTER |  |
| TIRES- RECORD PRESSURE & TREAD REMAINING BELOW: |  | RUN ENGINE TO CHECK FOR FUEL & OIL FILTER LEAKS |  |
|  |  | BLEED AIR FROM LUBRIFINER |  |
|  |  | CHECK AIR INTAKE PIPES AND CONDITION |  |
|  |  | CHECK AIR CLEANER RESTRICTION GAUGE, IF INDICATOR IS TRIPPED OR RESTRICTION IS 20 INCHS – PEPLACE FILTER |  |
|  |  | SAFETY INSPECTION EXPIRY DATE_________ |  |
|  |  | INSPECT COOLANT- RECORD READING_________ |  |
|  |  | ADJUSTMENT MADE_____ ADJUSTMENT NOT REQUIRED_______ |  |
|  |  | HYDRAULIC: |  |
|  |  | CHECK FLUID LEVEL |  |
|  |  | CHECK HOSES (NO CRACKS IN RUBBER COVERING OF HOSE) |  |
|  |  | CYLINDER LEAKS |  |
|  |  | CYLINDERS, CHECK PINS AND BUSHINGS, LUBRICATE |  |
|  |  | PTO OPERATION |  |
|  |  | TAILGATE HINGES |  |
|  |  | TAILGATE LOCKS |  |
|  |  | TANK VALVES |  |
| BATTERY INSPECTION |  | GAUGES |  |
| CHECK CABLES FOR CORROSION & TIGHTNESS |  | CHANGE HYDRAULIC FILTERS EVERY 500 HOURS |  |
| CHECK BATTERY HOLD-DOWNS & BOX MOUNTING |  |  |  |
| LUBRICATION |  |  |  |
| LUBRICATE CHASSIS & ACCESSORIES |  |  |  |
| LUBRICATE DOOR HINGES, LATCHS & LOCKS |  |  |  |
| LUBRICATE 5TH WHEEL CAM PLATE |  |  |  |
| LUBRICATE CAB-OVER HOLD DOWN LOCKS |  |  |  |
| INSPECT & LUBE ROLL-UP DOOR HINGES |  |  |  |
| LUBRICATE BRAKE CLEVIS PINS |  |  |  |
| CHECK ENGINE OIL LEVEL |  |  |  |
| CHECK FRONT WHEEL OIL LEVEL |  |  |  |
| CHECK TRANSMISSION OIL LEVEL |  |  |  |
| CHECK DIFFERENTIAL OIL LEVELS |  |  |  |
| INSTALL NEXT SERVICE STICKER |  |  |  |

# Text boxes

TIRE PRESSURE

TREAD 32NDS

REMARKS: