| Waste branch for basin | 1 no. | 32 mm |
| --- | --- | --- |
|  | 2-3 no. | 40 mm |
|  | 4-5 no. | 50 mm |
|  | 5 or more | 65 mm |
| Waste branch for each kitchen sink |  | 40 mm |
| Waste branch for each floor drain in toilet |  | 50 mm / 40 mm |
| Vent branch for each water closet |  | 50 mm |
| Vent branch for each urinal |  | 40 mm |
| Soil branch for each water closet |  | 100 mm |
| Soil branch for urinal | 1 no. | 40 mm |
|  | 2-3 no. | 50 mm |
|  | 4-6 no. | 65 mm |
|  | 7 or more | 80 mm |