# ACTIVE CROSSOVER

CX-152

## CX-153

## CX-154

REFERENCE

MANUAL

OPERATION

***** READ BEFORE USING *****

Caution: The following must be observed to prevent malfunctioning and /or possible equipment damage.

1 .Before plugging the unit into the main AC line, make sure that all of the equipment following the crossover output lines is turned off or all of the inputs are turned down.

2.The unit should be plugged in only when it has been established that main AC line is supplying the correct voltage and frequency.

3.Never change the frequency range switch from the x10 to x1 position (or vice versa) with the crossover output levels passing signal. Transients can result and speaker damage is possible.

Description

The CX-152, CX-153 and CX-154 are fourth order Linkwitz-Riley electronic crossovers. These units can be used in a wide variety of operation models, as shown below.

CX-152	CX-153	CX-154

STEREO 2-WAY        STEREO 3-WAY       STEREO 4-WAY

MONO 3-WAY	MONO 4-WAY

All inputs and outputs are floating and balanced when connected (via a tip, ring,) to other floating and balanced equipment. Any combination of balanced and unbalanced operation is permitted.

(1 )Power switch

(2)Channel 1 input level

(3)Channel 1 sub control

(4)Channel 1 sub-mid crossover frequency

(5)Channel 1 low control

(6)Channel 1 low-mid crossover frequency

(7)Channel 1 mid control

(8)Channel 1 mid-high crossover frequency

(9)Channel 1 low-high crossover frequency

(10)Channel 1 high control

(11)Channel 2 input level

(12)Channel 2 sub control

(13)Channel 2 sub-mid crossover frequency

(14)Channel 2 low control

(15)Channel 2 low-mid crossover frequency

(16)Channel 2 mid control

(17)Channel 2 mid-high crossover frequency

(18)Channel 2 low-high crossover frequency

(19)Channel 2 high control

(20)sub/low/mid/high mute switch

(21)sub/low/midlhigh clipping indicator

(22)Channel 2 high output

(23)Channel 2 mid output

(24)Channel 2 low output

(25)Channel 2 sub output

(26)Channel 2 line input

(27)Channel 1 high output

(28)Channel 1 mid output

(29)Channel 1 low output

(30)Channel 1 sub output

(31)Channel 1 line input

(32)sub/low/mid/high phase inversion switch

(33)Channel CD boost

(34)Channel crossover frequency x1/xl0 selection switch

(35)mono/stereo mode selection switch

(36)Ac line voltage selector

(37)Fuse holder

(38)Power cord

The constant directivity horn equalization circuit is to be used with horns that require a high frequency boost. Consult your horn manufacturer to determine whether it is needed in your circumstance. The provided boost is +3 db @ 3.5kHz rising 6 db per octave to 22.5kHz. (see figure 1) No changes need to be made to operate without the constant directivity boost.

If the constant directivity equalization circuit is desired on a particular channel then depress the corresponding switch labeled “CD BOOST”.

There is one switch for each channel located by that channels input jack. If two or more channels are ganged together, then only use the switch closest to the used input jack. The switches closest to the un-used input jacks have no effect on the circuit when ganged.

Clip LED

This LED will light when output capability is being exceeded with clipping distortion. Occasional flickering of the Clip LED is acceptable, but if it remains on continuously you should turn down the level control or reduce the output level of the preceding component to avoid audible distortion.

Range x10 (only CX-152)

When this switch is set on the cut off frequency adjusted by the High/Low FREQUENCY ADJUST knob is

multiplied by 10.

ON(FX10):	800Hz-9200Hz

OFF(FX1):	800Hz-920Hz LOW/MID/HIGH PHASE inversion switch

These switches invert an phase between the speakers. Use them when you feel a bad sound continuity between the LOW ,MID and HIGH ranges.

LOW SUMMING

The CX-152, CX-153 and CX-154 are designed to sum all or any of the low outputs if desired.

The shorting connector “CN4” must be removed from the channels being summed and should, for best results, be in place when no summing is desired. Shorting connector “CH4” is located nearly in the center at the two pieces board. You can easy to find it while the top plate opened.

CX-152 STEREO TWO-WAY

When stereo two-way operation is desired with the CX-152 there are no patch cords required.

Plug the left line-in and the right line-in to INPUT 1 and INPUT 2 respectively. From the LOW OUT 1 and

LOW OUT 2 attach a cable to the input of the left and right low frequency amplifiers. From the HIGH OUT 1

and HIGH OUT 2 attach a cable to the input of the left and right high frequency amplifiers.

RIGHT	LEFT

SOURCE

LINE-IN

RIGHT

LEFT

CX-152 MONO THREE-WAY

When mono three-way operation is desired with the CX- 152 there is no patch cords required. Plug the line-in

into INPUT 1. Attach cable from LOW OUT 1 to the low frequency amplifier. Do not anything into HIGH

OUT 2 or INPUT 2. Mode switch push mono. These jacks are automatically normalled when nothing is plugged

into them. Attach a cable LOW OUT 2 to the midrange amplifier. Attach a cable from high to the high

frequency amplifier.

(CAUTION: JUST PLACE INTO MONO ON MODE SWITCH PUSH.)

INPUT 1-	MAIN INPUT LEVEL CONTROL
LOW 1-	LOW FREQUENCY AMPLIFIER LEVEL CONTROL
HIGH 2-	SET TO 0 AND HIGH MUTE
FREQUENCY 1-	SET TO “X1” LOW/MID FREQ. CONTROL
INPUT 2-	SET TO 0
LOW 2-	MID FREQUENCY AMPLIFIER LEVEL CONTROL
HIGH 2-	HIGH FREQUENCY AMPLIFIER LEVEL CONTROL
FREQUENCY 2-	SET TO “X 10” MID/HIGH FREQ. CONTROL

RIGHT	LEFT	RIGHT LEFT	RIGHT

SOURCE

LI NE-IN

CX-153 STEREO THREE-WAY

When stereo three-way operation is desired with the CX-153. There are no patch cords required. Plug the left line-in and the right line in to input 1 and input 2 respectively. From the LOW OUT 1 and LOW OUT 2 attach a cable to the input of the left and right low frequency amplifiers. From the MID OUT 1 and MID OUT 2 attach a cable to the input of the left and right mid frequency amplifiers. From the HIGH OUT 1 and HIGH OUT 2 attach a cable to the input of the left and right high frequency amplifiers.

LEFT

CX-153 MONO FOURTH-WAY

When mono fourth-way operation is desired with the CX-153 there is no patch cords required. Plug the line-in

into INPUT 1. Attach cable from LOW OUT I to the sub frequency amplifier. Do not anything into HIGH

OUT 1 or INPUT 2. Mode switch push mono .These jacks are automatically normalled when nothing is plugged

into them. Attach a cable LOW OUT 2 to the LOW amplifier. Attach a cable from MID 1 to the midrange

frequency amplifier. Attach a cable from HIGH 1 to the high frequency amplifier.

(CAUTION:JUST PLACE INTO MONO ON MODE SWITCH PUSH.)

INPUT 1- MAIN INPUT LEVEL CONTROL

LOW 1 - SET TOO, and LOW 1 MUTE

MID 1- MID FREQUENCY AMPLIFIER LEVEL CONTROL

HIGH 1-HIGH FREQUENCY AMPLIFIER LEVEL CONTROL

LOW/MID FREQ. 1-MID OUTPUT RANGE, LOW CUT OFF FREQUENCY.

MID/HIGH FREQ 1- MID/HIGH FREQ.

INPUT 2- SET TO 0

LOW 2- SUB FREQUENCY AMPLIFIER LEVEL CONTROL

MID 2- LOW FREQUENCY AMPLIFIER LEVEL CONTROL

HIGH 2- SET TO 0 AND

LOW/MID FREQ 2- SUB/LOW FREQ.

MID/HIGH FREQ 2- LOW OUTPUT RANGE, HIGH CUT OFF FREQUENCY

RIGHT	LEFT	RIGHT LEFT	RIGHT LEFT	RIGHT LEFT

CX-154 STEREO FOURTH-WAY

When stereo fourth-way operation is desired with the CX-154. There are no patch cords required. Plug the left line-in and the right line in to input 1 and input 2 respectively. From the SUB OUT 1 and SUB OUT 2 attach a cable to the input of the left and right sub frequency amplifiers. From the LOW OUT 1 and LOW OUT 2 attach a cable to the input of the left and right low frequency amplifiers. From the MID OUT 1 and MID OUT 2 attach a cable to the input of the left and right mid frequency amplifiers. From the HIGH OUT 1 and HIGH OUT 2 attach a cable to the input of the left and right high frequency amplifiers.

specifications

Frequency Response

Low Frequency Output +0 -0.5 dB 10 Hz High Frequency Output =0-1 dB 20 kHz Total Harmonic Distortion

RL> 2 kohms

Low Frequency Output <0.01% THD High Frequency Output <0.02% THD Maximum Output Level

RL> 2 kohms	+21 dBu (6.2 volts) @
	<.05% THD 20-20 kHz

Maximum Voltage Gain 6 dB

Constant- Directivity Correction +3 dB @ 3.5kHz rising at 6 dB/octave to 22.5 kHz

| CX-152 | CX-154 |
| --- | --- |
| Frequency Range | Frequency Range |
| X1 80Hz to 920Hz | Sub-Low 15Hz to 92 Hz |
| X2 800Hz to 9.2kHz | Low-Mid 90Hz to 900 Hz |
| Hum and Noise (20 Hz - 20 kHz) | Mid-High 800Hz to 8 kHz |
| Av =0dB, fc=800Hz | Hum and Noise (20 Hz - 20 kHz) |
| Low Frequency Section | Av =0dB, fc=46,200,1k,5kHz |
| Output @ 0 dB <-106 dBu | Sub Frequency Section |
| High Frequency Section | Output @ 0 dB <-95 dBu |
| Output @ 0 dB <-97 dBu | Low Frequency Section |
| Signal to Noise Ratio 118 dB | Output @ 0 dB <-94 dBu |
| Controls | Mid Frequency Section |
| Input Level Continuously variable | Output @ 0 dB <-94 dBu |
| Output Level Low, High Cont. Variable | High Frequency Section |
| CD Boost Rear panel switch | Output @ 0 dB <-92 dBu |
| Mute Front panel switch | Signal to Noise Ratio 114 dB |
| Channel Link Rear panel switch | Controls |
| phase Rear panel switch | Input Level Continuously variable |
|  | Output Level Sub, Low, Mid, High Cont. Variable |
| CX-153 | CD Boost Rear panel switch |
| Frequency Range | Mute Sub, Low, Mid, High front panel switches |
| Low-Mid 100Hz to 920Hz | phase Low, Mid, High rear panel switches |
| Mid-High 800Hz to 9.2kHz |  |
| Hum and Noise (20 Hz - 20 kHz) |  |
| Av =0dB, fc=230, 2.3 kHz |  |
| Low Frequency Section |  |
| Output @ 0 dB <-98 dBu |  |
| Mid Frequency Section |  |
| Output @ 0 dB <-95 dBu |  |
| High Frequency Section |  |
| Output @ 0 dB <-93 dBu |  |
| Signal to Noise Ratio 114 dB |  |
| Controls |  |
| Input Level Continuously variable |  |
| Output Level Low, High Cont. variable |  |
| CD Boost Rear panel switch |  |
| Mute Low, Mid, High front panel switches |  |
| Channel Link Rear panel switch |  |
| phase Rear panel switches |  |