VHS 2 DVD-Video 

All VHS source should be interlaced video when capturing. However, should the user decide on the quickest method for transfer of VHS to DVD then I would recommend PowerVCR II Delux 3.0 as the best mpeg2 video quality capturing utility and WinDVD Recorder as the most DVD compliant mpeg2 capturing utility. 

The Quick Method 

PowerVCR II Settings 

Custom Profile 







Recording/Advanced 



STEPS 

1. Capture in Cyberlink PowerVCR II 
2. Demux to elementary streams with TMPGEnc* 
3. Convert MP2 to WAV with dBpowerAMP* 
4. Resample, clean, and normalize audio w/ Adobe Audition 
5. Convert WAV to Dolby Digital AC3 using any AC3 utility 
or 
Convert WAV to MP2 using dBpowerAMP 
6. Author with TMPGEnc DVD Author 
7. Preview with PowerDVD 
8. Burn with InstantCopy or DVDShrink 

Provisor: Cyberlink PowerVCR II captures progressive MPEG-2 and 44.1 khz audio. I do not suggest attempting captures of VHS to interlaced MPEG-2. I have had zero success capturing to interlaced MPEG-2 where audio and video remained in sync. An alternate program that allows for capture to progressive MPEG-2 with lesser video quality but a correct audio sampling rate is Intervideo WinDVD Recorder. WinDVD Recorder also allows you to capture AC3 audio. In the event you capture to AC3 and desire to clean the audio or cut any video from the project, then use DVD2AVI to extract audio, TMPGEnc MPEG Tools to extract video, and BeSweet to convert ac3 to wav. Clean the wav, mux to video, and cut using MPEG Tools. Should you desire to skip cleaning your audio and you have captured to ac3, an alternative to MPEG Tools is Cutterman. Cutterman requires .NET technology and is capable of cutting and appending mpg with ac3 audio. Should the user desire to add transitions or any effects to the video, then MPEG-2 should not be used as a transferring format. Please transfer your video to AVI. 

*Note: Should you have A/V sync issues after primarily demuxing your progressive mpeg file into mp2 and m2v elementary streams and secondarily resampling the audio to 48 khz, then I suggest as your primary step to encode your mpeg as a program/system stream with audio resampled to 48 khz wav and secondary step to demux the new stream into m2v and wav elementary streams. It seems that resampling the audio on-the-fly to an elementary stream or demuxing and then resampling, can cause sync issues. Encoding A/V data while resampling audio on-the-fly to a program/system stream keeps the A/V in sync: no issues should arise from subsequent cleaning or cutting. Be sure to encode to Half-D1 if so desired. 

The Thorough Method (NTSC Only) 

PREPARING FOR TRANSER 

Install AVISYNTH 
Install a DV Codec (Panasonic is RGB and Canopus is YUY2) 
Install Convolution3D (YUY2) to system32 folder 
& 
Install trbarry's Reinterpolate411 (4:1:1 Colorspacing) to system32 folder 

TRANSFERING A/V DATA 

Capture Type-2 AVI using ScenalyzerLive to C:\Movie Conversion as capture.avi 

WRITING YOUR DIGITAL NOISE REDUCTION AVISYNTH SCRIPT 

Verify field order of transfer data by loading in TMPGEnc XPress. 
Open Notepad and create your avisynth script, saving the file as Convolution3D.avs 

If your A/V data is Bottom Field First, use the following synth script: 

LoadPlugin("Convolution3d.dll") 
LoadPlugin("Reinterpolate411.dll") 
avisource("C:\Movie Conversion\capture0001.avi") 
ConverttoYUY2(interlaced=true) 
ReInterpolate411() 
Trim(x,y) // Do Not Add This Line Until After Loading in VirtualDubMod 
crop(8,2,-8,-14) 
SeparateFields() 
odd=SelectOdd.Convolution3D (0, 32, 128, 16, 64, 10, 0) 
evn=SelectEven.Convolution3D (0, 32, 128, 16, 64, 10, 0) 
Interleave(evn,odd) 
Weave() 
DoubleWeave.SelectOdd() 
AddBorders(8,8,8,8) 
BilinearResize(352,480) 

If your A/V data is Top Field First, simply remove the following line from your script: 

DoubleWeave.SelectOdd() 

If your A/V data is Progressive, simply use the following lines in your script: 

ConverttoYUY2() 
ReInterpolate411() 
crop(8,2,-8,-14) 
Convolution3D (0, 32, 128, 16, 64, 10, 0) 
AddBorders(8,8,8,8) 
BilinearResize(352,480) 

Provisor: The above synth script is written for a 720x480 Source Aspect Ratio. The source is cropped to 704x464 to remove black bar horizontal and rainbow vertical overscan. Borders are added to return the resolution to its SAR. Resizing to Half-D1 resolution from a 720 SAR uses 3:1 compression and will sacrifice the Pixel Aspect Ratio. Sacrificing PAR causes blur to occur in the resulting image. However, sacrificing PAR maintains the Displayed Aspect Ratio on DVD Standalone Player playback by a total 16 horizontal pixels. The amount of blur incurred by sacrificing PAR for DAR is minimal. Nevertheless, should one decide to sacrifice DAR for PAR, using AddBorders(0,8,0,8) and a 704 horizontal SAR, resizing to Half-D1 resolution [ie. LanczosResize(352,480)] will result in a sharper image with 2:1 compression. Ultimately, in using Half-D1 resolution either DAR or PAR must be sacrificed. The only way to maintain PAR and DAR is to use Full-D1 resolution and 1:1 compression. To maintain as close as possible the PAR when resizing from a 720 SAR, it is better to use BilinearResize in place of LanczosResize. 

If you decide on Full D1 resolution use the following script or no script: 

LanczosResize(720,480) 

Open Convolution3D.avs into VirtualDubMod and find your beginning frame and end frame points. Enter the beginning frame as value 'x' and end frame as value 'y' into the following line: 

Trim(344,22665) ++ Trim(32677,47725) ++ Trim(51051,77018) 

// The values shown are example points only 

Provisor: The sole purpose of using VirtualDubMod is to find the Trim points. All frames between trim points will be included in final video. Multiple trim points can be created to leave out unwanted scenes or commercials. 

ENCODING & DEMUXING 

Open Convolution3D.avs in Cinema Craft Encoder. 

Use following settings: 

ES VBR 2-pass MIN: 0 AVG: 3000 MAX: 4000 Half-D1 
ES VBR 2-pass MIN: 0 AVG: 6000 MAX: 8000 Full-D1 

Under Video: 

Closed GOPs 
If Top Field First, uncheck Upper Field First. * 
If Bottom Field First, check Upper Field First. * 

*Note: Passing your video data through the avisynth script may reverse the field order. It is necessary at this time to load your .avs synth script into TMPGXPress to verify the field order. 

Rename Audio to .wav for demuxing purposes. 

Under Quality: 

Interlaced 
Uncheck all boxes. 
DC Precision is 10 
Block Scanning Order should be ALTERNATE 
Flat Part Priority should be 16 

Progressive 
Uncheck all boxes except Progressive Frame Flag 
DC Precision is 10 
Block Scanning Order should be ZIGZAG 
Flat Part Priority should be 16 

Select ENCODE NOW. 

Your video and audio should be in elementary streams. 

CLEANING THE AUDIO 

There are three preset Adobe Audition filters I use to clean the audio. 

STEP 1 Noise Reduction Filter 
(Go to EFFECTS-->NOISE REDUCTION--> NOISE REDUCTION) 



The Noise Reduction function can dramatically reduce background and general broadband noise with a minimal reduction in signal quality. It can also remove tape hiss, microphone background noise, 60-cycle hum, or any noise that is constant throughout the duration of your waveform. The amount of reduction required depends upon the type of background noise, and the allowable loss in the quality of the signal that is to be kept. In general, you should be able to attain increases in Signal to Noise ratios of 5dB to 20dB. (Noise is reduced 21dB and signal 1dB for example). 

Before you can perform noise reduction, you must load or get a noise profile first. This is done by pressing the Load Profile or Get Profile from Selection buttons. 

Here’s the most common way to use the Noise Reduction function: 
1.Record or a piece of music that has tape hiss or other background noise. 
2.Select a short range (at least one half second) that contains only the noise that you'd like to reduce. 
3.Choose the Effects > Noise Reduction > Noise Reduction option and click on Get Profile from Selection to sample the noise. 
4.Click on Close. 
5.Select the entire file (or the portion you want to noise-reduce). 
6.Go to Effects > Noise Reduction >Noise Reduction again. 
7.Click on OK to perform the noise reduction. 

Preview 

Press the Preview button to audition the current Noise Reduction setting before you apply it to the waveform. The selection is looped until you press the Stop button. Since Previews are dynamic, this gives you the opportunity to make and hear processing adjustments as the selection is continuously played. 

STEP 2 Amplify (Go to EFFECTS-->AMPLITUDE-->AMPLIFY) 


Step 3 must be used when using Step 2 unless Peak is set to -1.89dB. 

STEP 3 Normalize Audio (Go to AMPLIFY-->NORMALIZE) 



Save Your Work! 

CONVERTING WAV to AC3/MP2 

AC3 is the standard for NTSC. 
MP2 is the standard for PAL, but does work on most NTSC DVD players. 
Do not convert to anything less than 256Kbps! Standard is 384Kbps. 

To convert to MP2, I use either dBpowerAMP or Besweet. The conversion is straight forward and should not necessitate a guide for completion. 

To convert to AC3 requires very expensive software. I have not had success with any of the freeware softwares though some users vouch for ffmpegGUI. Even this software has bugs, but offers the most compatible AC3 of the freeware programs. I suggest using a professional utility like Sony Acid Pro 4 for the creation of AC3 audio. Other AC3 programs include Sonic Foundry's Soft Encode and Scenarist's AC3Enc Utility. 

AUTHORING YOUR DVD 

I don’t make menus to increase compatibility in PS2 and Xbox playback; hence, I use TMPGEnc DVD Author even though movie-only can be done in other authoring softwares like DVDlab. I like DVD Author because it separates multiple titles into separate VTS sets unlike DVDlab that exports multiple titles to a single VTS/VOB set. I also prefer DVD Author over DVDlab because Author has the option to exports images and DVDlab does not. Finally, Author has a cut/editing option for the video that DVDlab does not. I add chapter points and write to disk as an image file. 

BURNING YOUR DVD 

For best quality use Pinnacle InstantCopy.* 
For quickest results use DVDShrink (possible loss of PS2 & Xbox compatibility).* 

*Note: It is always best to write/create an image file and preview your work before burning to disk. I simply export from TMPGEnc DVD Author to ISO and load using Daemon Tools and use PowerDVD to preview. InstantCopy, CloneDVD, and DVDShrink support ISO images when writing. Should you have exported to files or your authoring program does not offer image export, then an image can be created using IMGTools. Any and all errors occuring in playback will occur in Standalone playback. Do not question any errors or you will waste DVDR media. Check your work if any errors occur. 

Common Setting Errors Not Detected in PC Software Playback Include: 

1)Too low a video bitrate can cause interlaced video to produce interlaced lines and progressive video to hang or hiccup. 
2)Failure to synchronize correctly the source field order with the output field order, checking or unchecking UPPER FIELD FIRST in CCE, can produce ghosting in interlaced video. 
3)Audio compression below 192 kbps will not playback on a Standalone player. 

GUIDES USED 

Bb’s DV to DVD Guide 

FulciLives Digital Noise Guide 

SUGGESTIONS 

AN ALTERNATIVE TO ADOBE AUDITION: SONIC FOUNDRY SOUNDFORGE 

LordSmurf suggests the following use of Soundforge customized presets downloadable at above guide link: 

HISS CUT -or- HISS CUT ALT 2 -or- ALT 0 
NORMALIZE 80% 
then if still not fixed: 
HIGH RESTORE (any) ... if needed 
and HIGH RESTORE/HISS REMOVAL combo (any) ... if needed 

I am capturing via Canopus ADVC-100 Firewire. 
I especially like ScenalyzerLive and WinDV for firewire. 

I recommend Virtualdub 1.4.9.3 VCR + SYNC and VirtualVCR for transfering via Audio/Video PCI/AGP Cards. Visit www.doom9.org for these download. 

For ATI cards, stick with Lordsmurf at www.digitalfaq.com 

Both the Panasonic DV Codec and Canopus DV Codec are downloadable from www.videohelp.com under Tools. The Panasonic DV Codec is a .dll that comes with an .inf file. Right click on the .inf and click INSTALL. The Canopus DV Codec is self-extracting, although I had to place the setup files in a new folder as they would not execute in the folder created during the extraction. Reinterpolate411 can be downloaded from www.trbarry.com The convolution3D drivers can be downloaded from www.avisynth.org/warenterprises/ 

Take a look at bb's DV To DVD guide for other encoding options [ie. Procoder, TMPGEnc, MC Encoder.] 

As FulciLives suggests, should you decide to use XPress or DVD Source Creator for your encode an synth script can be used by adding the following line to the end of your synth script: 

ConverttoRGB(interlaced=true) 

If using QuEnc, requires Convolution3D YV12 , then add the following line to the end of your synth script: 

ConverttoYV12(interlaced=true) 

Please refer to bb's guide for all PAL Interlace, PAL Progressive and Type-1 AVI captures: these use the DirectShowSource in place of AviSource. I do not suggest capturing to Type-1 AVI, as it has filesize limitations, and suggest converting any Type-1 data to Type-2.