LBN ESSAY DIAGRAMS:

LBN ESSAY DIAGRAMS:

LBN ESSAY DIAGRAMS:

LBN ESSAY DIAGRAMS:

LBN ESSAY DIAGRAMS:

# Text boxes

Section thru log showing BACKING angles

# DECK angles

# Angles on

# ROOF plane

# COMMON rafter angle

= HIP rafter angle

## DIAGRAM 1

## ISOMETRIC SKETCH:

### Definitions and locations of angles

DIAGRAM 2

#### PLAN: 8/12 Rafters

#### meet Beams

(0, 1, 0)

# 90

# 45

cos 33.69007 = .83205

# R

# Pitch Angle of Corner Plane:

### arctan (1 / (1.5 / 2 ))

= 43.31386

(115/16 / 12 pitch)

# 8/12 Rafter

# 8/12 Rafter

# Beam

# Beam

# R

# P

# P

# Pitch Angle of 8/12 rafter:

### arctan (8 / 12)

= 33.69007

33.69007

BEAM

(0, 1, 0)

DIAGRAM 5

Inclined Deck and Vectors

a = (0, 1.83205, .55470)

b = (1.83205, 0, .55470)

r = (1.01624, 1.01624, -3.35641)

(1, 0, 0)

Convergence Vector or Line of Convergence:

Angle with respect to z axis = 23.18011

(-.83205, 0, -.55470)

DIAGRAM 3

Section R-R thru

8/12 RAFTER

1

(1, 0, 0)

(0, -.83205, -.55470)

BEAM

(1.01624, 1.01624, -3.35641)

r

sin 33.69007 = .55470

(0, -.83205, -.55470)

(-.83205, 0, -.55470)

8/12 RAFTER

y axis

x axis

DIAGRAM 4

Co-ordinates of Endpoints of

Unit Rafters and Unit Beams

8/12 RAFTER

b

a

z axis

#### DIAGRAM 6

Section P-P thru Corner Plane between 8/12 Rafters

Beam Plane

Rafter Plane

#### DIAGRAM 7

Inclined or Convergence Deck Projection

Beams lie on upper plane (level)

###### Total angle

###### = 43.31386

Actual or True Deck (level)

Inclined Deck

##### Total angle

= 46.68614 + 23.18011

= 69.86625

66.81989

23.18011

46.68614

23.18011

23.18011

20.13375

z axis

(plumb)

42.59146

42.59146

Rafter plane: Pitch angle = 20.13375

85.18292

37.77438

47.40854

42.59146

94.81708

52.22562

Beam plane:

Pitch angle = 23.18011

Common plane:

Pitch angle = 23.18011

Common plane:

Pitch angle = 23.18011

#### DIAGRAM 8

### Layout of Backing Angles

Section thru 8/12 Rafter, looking toward peak.

Common Plane

Rafter Plane

True Plumb:

Rotates to position when the logs are assembled. Any cuts required at rafter feet are with respect to this line.

Plane of Convergence thru Log Diameter:

(1) Starting from the log diameter, lay out the complements of the Inclined deck Backing angles.

(2) Lay out the complements of the Actual deck Backing angles, using the Roof plane edges as reference lines.

(1)

77.82791

(2)

60.98286

73.15496

90

16.84504

(1)

(2)

Ridge Line is fixed reference for both sets of Backing angles.

#### DIAGRAM 9

Sketch of ASSEMBLED JOINT

### Plan and Revolved Sections

8/12 RAFTER

8/12 RAFTER

BEAM

BEAM

Plane of Convergence thru Log Diameter

True Plumb

Ridge line, sum of Backing angles, and sum of Roof plane angles remain constant.

r

# Beam

# 8/12 Rafter