TIMBERS with NON-RECTANGULAR SECTIONS:

Vector Model

| Direction Numbers of Vectors |
| --- |
| Vector | x | y | z |
| a | 0 | sin  | sin tan  |
| b | 0 | sin  | 0 |
| c | cos sin tan tan  | sin  | sin tan  |
| d | cos  | sin  | 0 |
| e | cos  | sin  | sin tan  |
| f | cos sin tan tan  | 0 | 0 |
| g | sin tan tan  | 0 | sin tan  |
| Equivalent values: f X g = (1,0,0) b X d = (0,0,1) a X b = f = (1,0,0) |

VECTOR MODEL compared to SQUARE CUT MODEL:

Vector Model extracted and re-positioned,

with the magnitudes labeled.

“SLIDING” the VECTORS:

## Vector orientation or direction remains the

## same as in the original model.

| Simplified Table of Direction Numbers |
| --- |
| Vector | x | y | z |
| a | 0 | 1 | tan  |
| b ( = j) | 0 | 1 | 0 |
| c | 1 / tan tan tan  | 1 | tan  |
| d | 1 | tan  | 0 |
| e | 1 | tan  | tan tan  |
| f (= i) | 1 | 0 | 0 |
| g | 1 | 0 | tan  |
| k | 0 | 0 | 1 |
| i, to plane abk |
| j,  to plane fgk |
| k,  to plane bdi |
| tan   to plane dek |
| 0 tan   to plane aci ( = plane cef ) |
| -tan  tan tan   to plane cdg |

ROTATING the MODEL about the REFERENCE AXES:

Matrix for Projection of Points from the

Cross-Section (x y) Plane to the Compound (BEV) Plane

SUBSTITUE VALUES for TRIGONOMETRIC PROGRAMS:

Entries for XDIH, YDIH, and ZDIH < 90; if angles are  90, results may be supplementary or complementary to the values listed in the table. Certain entries (example: 4th row) return ambiguous values for MITER ONLY, or  = 90. To ensure accuracy, all results should be supplemented by 3-D models, and double-checked using vector analysis.

| ENTRIES | RETURNS |
| --- | --- |
| Main Side | Adjacent Side | Total Deck Angle | 90–P2 Main | 90–P2 Adjacent | 90–C5m + 90–C5a |
| XDIH | 90 -  | MIT | BEV |  | YDIH |
|  | ZDIH |  | MIT |  | 180 - XDIH |
| YDIH | 90 -  |  | BEV | MIT | XDIH |
| YDIH | XDIH | BEV |  | MIT | 90 -  |
| 180 - XDIH | ZDIH |  | MIT |  | 180 +  |
| 180 - XDIH |  | MIT |  |  | 180 + ZDIH |

| Table of Test Values |
| --- |
| Angle | General | Square Cut (XDIH = 90) | Miter only (ZDIH = 90) | Bevel only (YDIH = 90) |
|  | 20 | C5 | 20 | 20 | 20 |
|  | 60 | 90-R1 | 73.01695 | 90 | 60 |
|  | 50 | R4P | 50 | 50 | 90 |
|  | 15.44452 | P6 | 15.18892 | 15.57939 | 22.79588 |
| MIT | 45.40502 | P2 | 48.23670 | 51.74437 | 78.82977 |
| BEV | 55.80825 | 90-SS | 63.98951 | 74.42061 | 67.20412 |
| XDIH | 79.68680 | 90 | 90 | 77.29999 | 61.97568 |
| YDIH | 53.99479 | 90-DD | 51.25270 | 50 | 90 |
| ZDIH | 66.14135 | 90-A5P | 76.83217 | 90 | 60 |

# Text boxes

b

e   c

d = 1

f

a

Known Values:

Miter angle = 

Bevel angle = 

Slope angle = , the dihedral angle between the Sloped face and the face of Bevel angle .

Quantities to be calculated: MIT, BEV, and on the faces, and dihedral angles XDIH, YDIH, and ZDIH.

(= g)



g



MIT







(= c)

Equivalent to d = 1

BEV

XDIH : Dihedral angle between Sloped face and Compound face.

YDIH : Dihedral angle between Bevel (face and Compound face.

ZDIH : Dihedral angle between Miter () face and Compound face.

tan YDIH = tan sin 

tan ZDIH = tan sin 

cos(Compound Face Angle) = cos cos  BEV + 



Note the similarity between the geometries of the Vector Model for Non-rectangular Sections and the Alternate Model for Square Cuts, in fact, if XDIH = 90 degrees, the models are identical.



f = cos sin tan tan 

tan YDIH

= tan sin 

tan ZDIH

= tan sin 

# Dihedral angle

=  90 - 

cos 

b = sin 

It is possible to use combinations of MIT, BEV, and the dihedral angles as givens to calculate the remaining angular values, using either formulas, or a program that can solve standard timber framing angles. Refer to Alternate TFA Program Scenarios or the tables in this section.

k = sin tan 

BEV



d = 1

a = sin / cos 

a

MIT



Angle on

Compound Face







g

i

d

c

e

k

f

b

k

*g

sin tan tan 

*g = sin tan sin 

c



i

k

j

y

z

x

z

y

x

Original reference axes

c

g

- k





BEV





# ZDIH

YDIH

XDIH

Q

P

R

x, y co-ordinates : P = (0, 1)                                   x               y

Q = (1, 0)                   z  =

R = (1, 1 + tan ) cot cot 

g = Q – R              c = P – R

i             j           k         Solve quantities g, c and

r  =       xg         yg         zg            r = g X c (to BEV plane).

xc         yc         zc             c X - k (to MIT plane).

Unit vectors i, j, and k represent the remaining planes.

sin XDIH

= cos sin / sin BEV

k

j

The group of vectors drawn with heavier lines, which formed a Valley kernel in the initial diagram, are now arranged to create a Standard Hip Kerrnel.