GENERAL SQUARE CUT MODEL:

Refer to “Notes re: Square Cut Angles”

The square cut is extracted from the member, and a section is taken. Relationships between the angles are analysed, and a general model or template for any square cut may be created. Cognate angles, or angles in the same positions, may be substituted, the same as for tetrahedral kernels.

The angles along the bottom edge of Common Rafter meets Valley will be used as a template.

This geometric model is useful for dimensioning tenons, housings and mortises.

GENERAL SQUARE CUT MODEL:

#### Scaled in terms of Trig Functions of the Angles

| Type of Joint | Position | Miter | Bevel | SETS of SQUARE CUT ANGLES: Rafter meets Valley, cut along bottom edge to be used as template. Refer to diagrams for angle locations. |
| --- | --- | --- | --- | --- |
| Rafter meets Valley | Rafter bottom edge | P2 | 90-SS | C5 | 90-DD | 90+ A5P | 90-R1 | R4P | P6 | 90+ R5P |
|  | Plumb line (90-SS) | 90-SS | P2 | DD | 90-C5 | 90+ P5BV | 90-R1 | 90-A7 | P5 | 90+A9 |
| Purlin meets Valley | Purlin bottom edge | 90-P2 | 90-P1 | C5 | 90-C1 | 90+C2 | 90-R2 | 90-R3 | P3 | 180-Q2 |
|  | Ref. Line (90-R2) | 90-P1 | 90-P2 | C1 | 90-C5 | 90+ P4BV | 90-R2 | Q1 | P4 | 90+A8 |
| Valley meets Main Rafter | Valley bottom edge | R4P | 90-R1 | A5P | 90-DD | 90+ R6PBV | 90-R5P | VC | R6P | 90+ R1-R6P |
|  | Plumb line (90-R1) | 90-R1 | R4P | DD | 90-A5P | 90+ A5B | 90-R5P | 90-R5B | R4B | 180-(R4B+R4P) |
| Valley meets Main Purlin | Valley bottom edge | 90-R3 | 90-R2 | C2 | 90-C1 | 90+ R7BV | Q2 | VP | R7 | 90+ R2-R7 |

Note the interchange of Miter and Bevel, and their corresponding dihedral angles, for pairs of related square cuts on the same member; also, the angle on the Compound face stays constant.

# Text boxes

Square cut: Rafter meets Valley, extracted and sectioned

90-R1

Dihedral angle = 90-C5

P6

90-R1

90+R5P

C5

Dihedral angle = 90+A5P

R4P

Dihedral angle = 90-DD

Miter = P2

Square cut:

model re-oriented, Rafter meets Valley, showing locations of angles

90-SS

### Bevel =

(Dihedral angle)

90-SS

P2

Dihedral angle = 90-DD

Miter = P2

Bevel =

90-SS

Dihedral angle = C5

Dihedral angle = 90 degrees : The rafter is rectangular in cross-section. With modification, a similar model also serves for cuts on members non-rectangular in section, where the indicated dihedral angle is not 90 degrees. The values of any dihedral angles in the model may be supplementary to the value calculated by the formula.

tan C5

1 / cos C5 sin P2

The theoretical model “housing depth” is assigned a unit value, but may be set to any desired value in order to calculate actual mortise or tenon dimensions. The measurement in question is taken perpendicular to the face to be mortised.

1 / cos C5

tan C5 / cos R1

Housing Depth = 1

Calculations for R4P:  Miter (P2) and bevel (90-SS) are always given, the angle may be calculated using the following pattern:

Dihedral angle = 90-DD: tan(90-DD) = tanP2 / sin(90-SS)

Angle on Compound face = 90-R1: cos(90-R1) = cosP2 cos(90-SS)

tanR4P = tan(90-DD) sin(90-R1)

The angles on this plane may be identified by their position; in this case the plane follows the bottom face of the Valley rafter.

90-R1

1 / cos C5 tan P2

tan (Dihedral angle)

= tan (90-C5)

= tan (90-SS) / sin P2

tan (Dihedral angle)

= tan (90-DD)

= tan P2 / sin (90-SS)

= tan R4P / sin (90-R1)

tan (Dihedral angle)

= tan (90-A5P)

= tan (90-R1) / sin R4P

1 / sin R4P

1 / tan R4P

A scalene triangle is formed by the dihedral angle being projected to the side face of the rafter. Values may be calculated from known angles using the Law of Cosines.